## Slide 1
Status and scientific capability of the
Einstein Probe mission
Image credit CAS/ESA
张文达
国家天文台
on behalf of the Einstein Probe consortium
银河系及近邻星系时域研讨会，丽江，3-7/8/2024

## Slide 2: Einstein Probe (EP) mission
Milestones
2010- Lobster-eye R&D @ XIL/NAO (est. by S.-N. Zhang)
2012 Mission concept
2017/12 Adoption
2018 Joined by ESA & MPE; 2022 CNES
2022/07 Pathfinder LEIA launched
2024 Jan. 9 launch
2024/07 nominal mission (lifetime: 3 yr, goal 5 yr)
Goals a time-domain astro. mission
Discover soft X-ray transients & monitor source variability with improved sensitivity
Characterise transients/variables by quick X-ray follow-up onboard
Disseminate transient alerts to astro. community in time

## Slide 3: Instruments & spacecraft
Wide-field X-ray Telescope
WXT (12 modules)
Follow-up X-ray Telescope
FXT (2 units)
Lobster-eye MPO + CMOS
FoV: ~3,600 sq deg (1.1 sr)
Band: 0.5 – 4 keV
Resolution: ~ 5’ (FWHM)
Sensitivity: ~1mCrab @1ks
Wolter-1 + pn-CCD (eROSITA)
FoV: ~1 deg
Band: 0.3 -10keV
Resolution: 24” (HPD, on-axis)
Effe. area: ~300 cm2 @1keV (x 2 units)
Yuan, et al. 2022 Handbook of X-ray and Gamma-ray Astrophysics
On-board data processing
Quick slew & autonomous follow-up
Spacecraft
X/S-band (several hours)
BD (down/up-link; minutes)
VHF (down-link; minutes)
Telemetry
WXT mirror & CMOS detectors (1 module)

## Slide 4: EP-WXT pathfinder LEIA (Lobster Eye Imager for Astronomy)
Instrument test observations
August 8-10, 2022
~800s exposure
Size of full Moon
FoV 340 deg2
Frist wide FoV X-ray observations by a lobster-eye focusing X-ray telescope in orbit Zhang et al. 2022 ApJL, 941, L2
Lobster-eye & CMOS technology verified
CAS’s SATech-01 experiment satellite
Launched 2022-07-27
credit: MicroSAT
LEIA 0.5 – 4 keV

## Slide 5: Launch of EP Jan. 9, 2024
LM-2C @Xichang
  height 592 km
  orbital period 96min
  inclination angle 29 deg.
  height 592 km
  orbital period 96min
  inclination angle 29 deg.
Launch of EP Jan. 9, 2024

## Slide 6: Launch of EP Jan. 9, 2024
  height 592 km
  orbital period 96min
  inclination angle 29 deg.

## Slide 7: Commissioning phase just completed
Payloads & SC: In-orbit tests, verifications and calibration just almost completed and passed review
  Spacecraft and payloads
  Satellite-ground interface & workflow（S/X-band, VHF, BD short-message system)
Onboard transient search, triggering, and automated FXT follow-up obs. achieved
Spacecraft & instruments working normally
  some minor anomalies are being resolved/improved
In-orbit/on-ground calibration results agree
Start of science operations: July 10 (nominal: end of July)

## Slide 8
X-ray data credit: EPSC, image credit: Chen Zhang, Huaqing Cheng.
Red: 450 to 1000 eV
Green: 1000 to 2000 eV
Blue: 2000 to 5000 eV
Energy (keV)
Counts/sec/keV
Si He 1.83
S He 2.41
Image size 9.3° X 9.3 °
exposure 22 kilo-seconds
X-ray First light 2024 Feb. 19
Cassiopeia A supernova remnant (nebula)
X-ray spectrum obtained at the same time
E ~ 122eV @1.25keV

## Slide 9
Red: 400 to 800 eV
Green: 800 to 1500 eV
Blue: 1500 to 5000 eV
9.3° by 9.3 °
X-ray data credit: EPSC, image credit: Chen Zhang, Huaqing Cheng.
Vela supernova remnant X-ray (nebula)
exposure 9.3 kilo-seconds
mage size 9.3° X 9.3 °
Vela supernova exploded about 11000 yr ago
936 light years to Earth

## Slide 10
Central region of our Galaxy
WXT covers 1/11 area of the entire sky in one snapshot
X-ray data credit: EPSC, image credit: Chen Zhang, Huaqing Cheng.

## Slide 11
10
1: Cir x-1 and Swift J151857.0-572147
2: Sco X-1
3: V2216 Oph
4: V1101 Sco
5: V821 Ara
6: NP Ser
7: V4134 Sgr
8: Sgr X-4
9: Lupus SN
10: SNR RCW 86
2
1
9
5
8
7
4
3
6
9.3°
Central region of our Galaxy (purple, red, yellow)
WXT FoV 3850 sq. deg.
X-ray data credit: EPSC, image credit: Chen Zhang, Huaqing Cheng.
exposure 40 kilo-seconds

## Slide 12
FXT X-ray First light
Crab nebula supernova remnant
Band 0.3-10 keV
Exposure 2600s
Crab pulsar spin period 33.98 ms
timing mode: time resolution 42 micro-sec

## Slide 13
FXT X-ray First light (0.3-10 keV)
Puppis A supernova remnant (nebula)
FoV 1 deg
FXT X-ray spectrum obtained at the same time

## Slide 14
EP240219a
The first X-ray transient discovered by WXT on Feb 19, 2024, alert released on Astronomer's Telegram
9.3° by 9.3 °, 1 time-frame = 33.3 sec
WXT 主任设计师 （上海技物所）
Duration < 200s
Subthreshold GRB signal found in Fermi/GBM data (Zhang ATel #16473)
Undetected by Swift/XRT 39 hours later
Atel sent from EPSC: 1st EP alert!
No optical counterpart found （starting T0+3days）
Possibly an X-ray rich GRB
Yin et al. ApJL submitted

## Slide 15: Onboard trigger for FXT automated follow-up
1st successful test: EP240605a June 5 UTC 16:10:30,
transient info downlink within minutes (BD & VHF)
triggered FXT obs @ UTC 16:11:44
  1 min after triggering
FXT X-ray lightcurve
flare star (FXT spec)
FXT X-ray image
alert information downlinked via BD
expo 3.6 ks
FXT error < 10arcsec

## Slide 16: EP240414a: the quickest follow-ups
WXT onboard trigger (VHF/BD)
  (Lian et al. GCN 36091)
T0+ 2hrs: FXT follow-up (uplink ToO)
  A new source 1.5’away
Optical follow-up
  LOT + 3.13 hr (AT2024gsa, r= 21.52 mag)
  NOT +2.29 hr
  GTC +5 hr
  BOOTES-4/MET +5.56 hr
  Pan-STARRS1 +2/3 d
  GSP + 3.66 d
Later time detection of associated supernova (Levan et al. GCN 36355)
Host galaxy z = 0.41
Projected offset ~25 kpc (Jonker et al. GCN 36110)
FXT image expo 7.2 ks
90% positioning errors
WXT: 2.1 arcmin
FXT: < 10 arcsec

## Slide 17: EP240315a: GRB @redshift 4.859
Onboard trigger, confirmed by on-ground analysis
Soft X-ray T90: 1000 s
Gamma-ray T90：<50 s
by Swift/BAT & Konus-Wind
Marked difference in LC of soft X-ray and hard X/γ rays
Gillanders J.H., et al. arXiv:2404.10660 (ATLAS optical/radio counterpart, z)
Levan A., et al. arXiv.2404.16350 (Stargate optical pho. and spec., z)
Liu Y., et al. arXiv:2404.16425 (jointly with Swift, Konus-Wind, Stargate teams)
FXT detection of X-ray afterglow
WXT image
redshift 4.859 measured by VLT (Levan et al. 2024)
detectable by WXT at z~7.5
EP’s potential of detecting high-z GRB !

## Slide 18: GRBs(4)/Fast X-ray transients (10) by EP & LEIA
Transient | Duration | Peak Flux erg cm-2s-1 | Fluence erg cm-2 | -ray counterpart | X-ray afterglow | Optical afterglow | z
LXT/GRB 230307A | ~180 s | 4E-7 | 2E-5 | Y | Y | Y | 0.065
EP240219a | ~200 s | 5E-9 | 1E-7 | Y | X | N | -
EP240315a | ~1600 s | 3E-9 | 1E-6 | Y | Y | Y | 4.859
EP240202a | ~300 s | 4E-9 | 9E-8 | N | N | N | -
EP240316a | ~160 s | 3E-9 | 1E-7 | N | N | N | -
EP240331a | ~100 s | 4E-9 | 2E-7 | N | possible? | N | -
LXT240402a | ~200 s | 3E-8 | 5E-7 | Y | Y | Y | 1.551
EP240413a | ~200 s | 7E-9 | 2E-7 | N | possible? | N | -
EP240414a | ~150 s | 3E-9 | 2E-7 | N (GBM off) | Y | Y | 0.4
EP240416a | > 200 s | 1E-9 | 1E-7 | N (GBM off) | N | N | -
EP240417a | > 1500 s | 3E-10 | 1E-7 | N | N | N | -
EP240420a | ~80 s | 8E-9 | 3E-7 | N | Y | Y | -
EP240426b | ~300 s | 9E-10 | 2E-7 | N | N | N | -
EP240506a | ~50 s | 1E-8 | 5E-8 | N | N | N | -
Transient | Duration | Peak Flux erg cm-2s-1 | Fluence erg cm-2 |  | X-ray afterglow | Optical afterglow | z
LXT/GRB 230307A | ~180 s | 4E-7 | 2E-5 | Y | Y | Y | 0.065
EP240219a | ~200 s | 5E-9 | 1E-7 | Y | X | N | -
EP240315a | ~1600 s | 3E-9 | 1E-6 | Y | Y | Y | 4.859
EP240202a | ~300 s | 4E-9 | 9E-8 | N | N | N | -
EP240316a | ~160 s | 3E-9 | 1E-7 | N | N | N | -
EP240331a | ~100 s | 4E-9 | 2E-7 | N | possible? | N | -
LXT240402a | ~200 s | 3E-8 | 5E-7 | Y | Y | Y | 1.551
EP240413a | ~200 s | 7E-9 | 2E-7 | N | possible? | N | -
EP240414a | ~150 s | 3E-9 | 2E-7 | N (GBM off) | Y | Y | 0.4
EP240416a | > 200 s | 1E-9 | 1E-7 | N (GBM off) | N | N | -
EP240417a | > 1500 s | 3E-10 | 1E-7 | N | N | N | -
EP240420a | ~80 s | 8E-9 | 3E-7 | N | Y | Y | -
EP240426b | ~300 s | 9E-10 | 2E-7 | N | N | N | -
EP240506a | ~50 s | 1E-8 | 5E-8 | N | N | N | -

## Slide 19: Example light curves of EP fast transients
only ~ 1/3 have hard X-ray/gamma-ray counterparts as GRBs；
what are the other 2/3?

## Slide 20: Statistics on X-ray sources detected with EP-WXT
            Known bright sources detected: ~5000
    Transients：> 44 high S/N (> 100 low S/N)
    Stellar flares：340
            More than 13,000 new sources found
WXT
FXT
            More than 50 GCN+Atel alerts
Alerts

## Slide 21: Detection of transients on a daily basis
3 transients found by EPSC on Aug. 3rd:
WXT detects two transients EP240802a (GCN 37019) and EP240802b
FXT also detects a new transient during the follow-up observation of EP240802a

## Slide 22: Galactic transients
WXT LC
EP240309a
A bright UV source and highly variable in optical (ATel #16554), MeerKAT obs. (ATel #16572)
a magnetic CV- intermediate polar
orbital period 3.76 hr, white dwarf spin 3.97min
(Potter 2024 MNRAS)
WXT LC
ATeL #16514
Swift/XRT
Swift-UVOT
late-A/early-F type star ACTA radio detection (ATel #16555)

## Slide 23: Search for potential X-rays from GW event S240422ed
On April 22, GW event NS+BH (>99%), 214 +/- 64 Mpc
EP observations: started ~ 3 hrs after GW trigger (yet to be improved)
Covered with WXT and set X-ray flux upper limits (GCN: 36270, 36277, 36282)
Searched >100 galaxies with FXT
Hu 2024 in prep.

## Slide 24: EP detects an outburst in Small Magellanic Cloud
CXOU J005245.0-722844 a weak Chandra source
WXT detected its first X-ray outburst (Atel#16631)
also by Swift/XRT (ATeL# 16633), follow-up by NICER (ATeL# 16636)
a possible rare Be-WD binary system
submitted to ApJL (arxiv:2407.21371)
Super-soft spectrum

## Slide 25: Conclusion
Since launch on January 9, EP’s performance verifications & calibrations have completed
Spacecraft & instruments working as expected
> 30 X-ray transients (>100 faint ones) were detected
Nominal science operations just started yesterday (practically)
A newcomer with great scientific potential in time-domain X-ray astronomy
http://ep.bao.ac.cn
https://www.esa.int/Science_Exploration/Space_Science/Einstein_Probe_factsheet
Thanks to the entire community and other mission teams for the welcoming, enthusiasm and help to EP mission,
particularly follow-ups with Swift, NICER, Chandra, XMM, etc. and ground-based optical and radio telescopes around the world …..

## Slide 26: Monitoring of known X-ray sources
X-ray binary
Seyfert galaxy AGN
blazar

## Slide 27: Perspectives on GRB research
About 2/3 of the EP fast transients have no significant gamma-ray counterparts
  detecting GRB in soft X-ray: follow on the legacy of Beppo-SAX and HETE-2
  previously scarcely detected population, X-ray flash, X-ray rich GRB, ….
Soft X-ray prompt emission (possible new insight into GRB central engine activity)
  more extended (longer T90)
  complicated structure, multiple peaks
EP240315a: demonstrating the potential in detecting high-z GRB
  faint flux end of known high-z GRB, detectable at z~7.5 (Liu Y. et al. 2024, Levan et al. 2024, Gillanders et al. 2024)

## Slide 28: Observation modes
Equatorial coordinates
Circular orbit
  Height 592km, period 96min
  inclination angle 29 deg.
Observation modes
  Survey (primary WXT)
  Autonomous follow-up (FXT)
  ToO (FXT, WXT)
  Calibration
WXT survey mode
  Pointing to night sky
  3 pointings/orbit, ~20min each
  ~ 1/2 sky covered in 3 orbits (~ 5 hr)
  Whole sky coverage in ½ year
  FXT pointed to pre-selected targets
Notes: ~ 45 snapshots per day
FXT survey target observation (FSTO)

## Slide 29: Alerts of transients, ToO & data
Transient alerts
  Onboard transient search and trigger unit
  Alert information quick downlink： minutes
    VHF (CNES/France)
    BD system (China)
  Alert information: release immediately to the community
    source position, flux, time, spectral parameter
ToO command uplink
  Normal (S-band): < 1 day
  Time critical (BD) < 10 min
Science data
  X-band telemetry: it takes about a few hours to reach EPSC
  Will be made public (community outside EPST) after proprietary periods
  Non-ToO data: one year
  ToO by EP science team: 6 months
  ToO by guest observers: released immediately

## Slide 30: Alerts of transients, ToO & data
Transient alerts
  Onboard transient search and trigger unit
  Alert information quick downlink： minutes
    VHF (CNES/France)
    BD system (China)
  Alerts info: release immediately to community (we’re working toward reducing latency)
    source position, flux, time, spectral parameter
ToO command uplink
  Normal (S-band): < 1 day
  Time critical (BD) < 10 min
Science data
  X-band telemetry: it takes about a few hours to reach EPSC
  Will be made public (community outside EPST) after proprietary periods
  Non-ToO data: one year
  ToO by EP science team: 6 months
  ToO by guest observers: released immediately

## Slide 31: EP data and information flows
EPSC

## Slide 32: EP main web page at NAOC

## Slide 33: Main science objectives
Discover otherwise quiescent black holes at almost all astrophysical mass scales and other compact objects by capturing their transient X-ray flares
Detect and localise the electromagnetic-wave sources of gravitational-wave events by synergy with gravitational-wave detectors
Systematic survey of soft X-ray transients and variability of X-ray sources with unprecedented combination of sensitivity and cadence

## Slide 34: Wide-field X-ray Telescope
one module
Flight model 17kg
Instrument scientist &
lead of CMOS
Zhxing Ling (NAO/CAS)
Lead of LE mirrors
Chen Zhang (NAO/CAS)
WXT chief designer
Xiaojin Sun (SITP/CAS)
MA engineer
Yanfeng Dai (NAO)
mirror assembly
detector array
MPO plates (developed by NNVT jointly with NAO/CAS)
41mm x 41mm each
BI CMOS sensors
Time resolution 50ms
E ~ 122eV @1.25keV

## Slide 35: Follow-up X-ray Telescope (FXT)
IHEP/CAS + ESA + MPE
2 Wolter-I mirror assemblies
  1 by ESA (Media-Lario, eROSITA design)
  1 by MPE (eROSITA FS)
X-ray cameras (IHEP)
  PN-CCD detector modules by MPE based on eROSITA tech.
PI: Yong Chen
(IHEP/CAS)
FXT mirror assembly FM
(ESA/MediaLario/MPE)
X-ray camera built @ IHEP/CAS
FXT Delivered by IHEP team to MicroSAT on May 26
E2E test/calibration @ IHEP/CAS 100m beamline
Camera lead:
Weiwei Cui (IHEP/CAS)

## Slide 36: EP satellite
S/C developed @ MicroSat/CAS, Integration & tests
acoustic test
thermal vacuum tests
thermal vacuum tests
just before launch